Journal "Chemistry and Technology of Organic Substances", N 2 (14) /2020

Section I. ORGANIC SYNTHESIS

Glukhan E.N., Belikov V.A., Kaabak L.V., Kondrat’ev V.B., Maliyova K.O.

Method for producing terephthalic acid by sequential oxidation of p-xylene with manganese dioxide and potassium permanganate under mild conditions

Federal state unitary enterprise «State scientific-research Institute of organic chemistry and technology» State Scientific Center of Russian Federation,

111024, Moscow, Shosse Entuziastov, 23,

e-mail: dir@gosniiokht.ru, tеl.: +7 (495) 673-78-26

Abstract

A method for producing terephthalic acid from p-xylene has been developed. The method allows the product to be synthesized under mild conditions, namely at atmospheric pressure and temperatures no higher than 90 °С. The process consists of two stages: by the first p-xylene is oxidized by manganese dioxide in a mixture of 35–60% sulfuric acid and 10–30% perchloric acid and then obtained intermediates are oxidized by potassium permanganate in an alkaline medium. The temperature range from 75 °C to 90 °C is optimal for the first stage of the synthesis. Regime of the first stage was selected based on the results of its thermochemical study by differential scanning calorimetry. The high efficiency of using of mixture of acids as a promoter of p-xylene oxidation in a wide range of their concentrations was confirmed. It was found that oxidation of the first stage products with potassium permanganate provides high-purity terephthalic acid (up to 99,9 %) with an output up to 86 % at the second stage. This method of synthesis of terephthalic acid can compete with currently used technologies for its production based on catalytic oxidation of p-xylene with by molecular oxygen under harsh conditions with using an organic solvent.

Keywords: p-xylene; oxidation; terephthalic acid; manganese dioxide; mixture of sulfuric and perchloric acids; potassium permanganate.

References

1. Nazimok V.F., Ovchinnikov V.I., Potekhin V.M. Zhidkofaznoe okislenie alkilaromaticheskih uglevodorodov. M.: Himiya, 1987. 240 s.

2. Reutov O.A., Kurc A.L., Butin K.P. Organicheskaya himiya, ch. 4. 2-e izd. M.: Binom, 2015. S. 612–614.

3. Patent 2292332 RU. MPK C07C 63/26, C07C 51/43, C07C 51/265. Sposob polucheniya ochishchennoj tereftalevoj kisloty / Lin R. (US), O’Meadhra R.S. (US), Sheppard R.B. (US). N 2003137848/04; zayavl. 04.06.2002; opubl. 27.01.2007. Byul. N 3.

4. Patent 2435753 RU. MPK C07C 51/16, C07C 51/26, C07C 51/42, C07C 51/265. Optimizirovannoe zhidkofaznoe okislenie / Uanderz A.D. (US), Lavua D.D. (US), Samner Ch.E. (US), Dejvenport B.U. (US), De Vrede M. (NL), Tennant B.A. (US). N 2008101655/04; zayavl. 24.05.2006; opubl. 10.12.2011. Byul. N 34.

5. Patent 2399610 RU. MPK C07C 51/235, C07C 51/265, C07C 63/26. Sposob polucheniya tereftalevoj kisloty vysokoj chistoty / Gronec M. (SK), Al’gatta H. (IT), Rudzhieri R. (IN). N 2008127885/04; zayavl. 09.12.2005; opubl. 20.09.2010. Byul. N 26.

6. Patent 2531906 RU. MPK C07C 51/21. Sposob polucheniya tereftalevoj kisloty / Bhattachariiya A.K. (US), Koukal D.A. (US), Valenga D.T. (US), Adonin N.Yu. (RU), Kuznecova N.I. (RU), Bal’zhinimaev B.S. (RU).N 2012151255/04; zayavl. 16.06.2011; opubl. 27.10.2014. Byul. N 30.

7. Patent 2599636 RU. MPK C07C 63/26, C07C 51/16, C07C 51/42, C07C 51/48, C07C 51/487. Sposob polucheniya ochishchennoj tereftalevoj kisloty / Hara N. (JP), Ito E. (JP), Yamadzaki H. (JP). N 2015102946/04; zayavl.29.01.2015; opubl. 10.10.2016. Byul. N 28.

8. Belikov V.A., Glukhan E.N., Kaabak L.V., Kondrat´ev V.B., Maliyova K.O. Thermochemical study of p-xylene oxidation with manganese dioxide under mild conditions // Chemistry and Technology of Organic Substances. 2019. N 4 (12). P. 4–13 (in Rus.).

9. Zayavka №2016134893 RU. MPK C07C 51/42. Sposob polucheniya tereftalevoj kisloty / Ivai H.(JP). Zayavl. 26.02.2015; opubl. 29.03.2018. Byul. N 10.

10. Patent 2671210 RU. MPK C07C 51/265, C07C 51/44, C07C 51/48, C07C 63/26, B01D 11/00. Poluchenie aromaticheskoj dikarbonovoj kisloty / Yure A.M. (GB), Limbech E.P. (GB) N 2017113539; zayavl. 23.09.2015; opubl. 30.10.2018. Byul. N 31.

11. Reutov O.A., Kurc A.L., Butin K.P. Organicheskaya himiya. 2-e izd. Tom 2. M.: Binom, 2014. S. 512, 551.

12. Bekker H., Bekkert R., Berger V. i dr. Organikum. 4-e izd. Tom 2: Per. s nem. Gryunera S.V. i Terent’eva P.B. M.: Mir, 2008. S. 10–14.

13. Razumovskaya M.T., Belyakova A.I., Korel’skaya G.I. Metody polucheniya himicheskih reaktivov i preparatov. M.: IREA. 1965. S. 96–100.

----------------------------------------------------------------------------------------------Malenkov M.Yu., Golovkov V.F., Kaabak L.V., Golikov A.G., Kuchinsky E.V., Martynov B.I., Gorelenko S.V.

N-chloromorpholine as promising electrofilic amination reagents

Federal state unitary enterprise «State scientific-research Institute of organic chemistry and technology» State Scientific Center of Russian Federation,

111024, Moscow, Shosse Entuziastov, 23, e-mail: dir@gosniiokht.ru, tеl.: +7 (495) 673-78-26

Abstract

Features of electrophylic amination of sodium polysulfides and

1-(N-morpholine)polysulphanes by N-chloromorpholine are issued. New chemical method of N,N-dimorpholineoligosulfides with medium product yield is suggested. The best reaction conditions are determined and possible reaction scheme is discussed.

Keywords: synthesis; amination; morpholine; harborton; polysulfides; oligothiophene; reaction cheme.

References

1. Obshchaya organicheskaya himiya / Pod red. D.Bartona i U.D.Ellisa. T. 3. Azotsoderzhashchie soedineniya / Pod red. I.O.Sazerlenda. Per. s angl. / Pod red. N.K.Kochetkova i L.V.Bakinovskogo. M.: Himiya, 1982. 736 s.

2. Accelerator DTDM. URL: https://www.buyersguidechem.com/ chemical_supplier_ru/Accelerator_DTDM (data obrashcheniya 12.01.2020).

3. Reutov O.A., Kurc A.L., Butin K.P. Organicheskaya himiya: v 4 ch. Chast’ 3. 4-e izd. M.: BINOM. Laboratoriya znanij, 2015. 544 s. ISSN 978-5-00101-508-6.

4. Sajks P. Mekhanizmy reakcij v organicheskoj himii / 4-e izd. Per. s angl. / Pod red. V. F. Travenya. M.: Himiya, 1991. Per. izd.: Velikobritaniya, 1986. 448 s. ISBN 5-7245-0191-0.

5. Volkov A.I., Zharskij I.M. Bol’shoj himicheskij spravochnik. Minsk: Sovremennaya shkola, 2005. 608 s. ISBN 985-6751-04-7.

6. Laboratornye i seminarskie zanyatiya po neorganicheskoj himii : ucheb. posobie dlya studentov himiko-tekhn. spec. vuzov / N.S.Ahmetov, M.K.Azizova, L.I.Badygina. M.: Vysshaya shkola, 1979. 255 s.

7. Glinka N.L. Obshchaya himiya: ucheb. posobie dlya vuzov / pod red.: A.I.Ermakova. 30-e izd., ispr. M.: Integral-Press, 2003. 461 s. ISBN 5-89602-017-1.

8. Oae S. Himiya organicheskih soedinenij sery. M.: Himiya, 1972. S. 62–108.

_______________________________________________________________

Section II. TECHNOLOGY OF ORGANIC SUBSTANCES

Коmissarova G.М., Belyaev E.L., Smirnov М.К., Golubeva Yu.Yu., 
Pavlova N.А., Vlasova Z.V., Polikanova А.S., Коndrat’ev V.B.

Methods for preparing modified liquid compositions based on 
4,4′-diphenylmethane diisocyanate in the conditions of small-scale production

Federal state unitary enterprise «State scientific-research Institute of organic chemistry and technology» State Scientific Center of Russian Federation,

111024, Moscow, Shosse Entuziastov, 23, e-mail: dir@gosniiokht.ru, tеl.: +7 (495) 673-78-26

Abstract

Two economical techniques for the preparation of liquid compositions on the basis of diphenylmethane diisocyanate are worked out. The first one involves the production of mixtures of 2,2′-, 2,4′- and 4,4′-diphenylmethane diisocyanate isomers of definite composition; the second one involves heat treatment of 4,4′-diphenylmethane diisocyanate under certain conditions which allows its crystal structure to be disrupted. Optimum conditions for the syntheses of the mentioned liquid compositions are determined for the purpose of their realization on the experimental-industrial setup for the isocyanate production.

Keywords: isocyanate composition; diaminodiphenylmethane; carbonyl chloride; uretonimine; phospholene oxide.

References

1. Gorbatenko V.I., Zhuravlev E.Z., Samaraj L.I. Izocianaty. Metody sinteza i fiziko-himicheskie svojstva alkil-, ariligeterilizocianatov. Kiev: Naukova dumka, 1987. 448 s.

2. Six C., Richter F. Organic isocyanates // Ullmann’s Encyclopedia of Industrial Chemistry, Wiley-VCH, 2002. Vol. 20. P. 63–82. DOI: 10.1002/14356007.o17_o02.

3. Gorbunov B.N., Gurevich Ya.A., Maslova I.P. Himiya i tekhnologiya stabilizatorov polimernyh materialov. M.: Himiya, 1981. 368 s.

4. Verardo G., Cauchi S., Guimanini A. Observation of a stable monomeric 
N-methylene aromatic amine // Journal of the Chemical Society. Chemical Communications. 1985. N 24. P. 1787–1788. DOI: 10.1039/ C39850001787.

5. Wang C., Li H., Wang L., Cao Y., Lui H., Zhang Y. Insights on the mechanism for synthesis of methylenedianiline from aniline and formaldehyde through HPLC¨CMS and isotope tracer studies // Chinese Chemical Letters. 2012. Vol. 23. N 11. P. 1254–1258.

6. Perego C., de Angelis A., Carati A., Flego C., Millini R., Rizzo C., Be-lussi G. Amorphous aluminosilicate catalysts for hydroxyalkylation of aniline and phenol // Applied Catalysis: A. General. 2006. Vol. 307. P. 128. DOI: 10.1016/j. apcata.2006.03.013.

7. Patent US3676497A C07C209/78. Process for preparing di(aminophenyl)-methanes / F. P. Recchia, H. Ulrich; Dow Chemical Co. Appl. 1968-08-06; publ. 1972-07-11.

8. Patent US3277173A C08G18/7664. Process for preparing aromatic polyamines / Eu.L. Powers I.B. Van Horn; Mobay Corp; Appl. 1963-06-13; publ. 1966-10-04.

9. Himicheskie reakcii polimerov: v 2 t. / pod. red. E. Fettesa, per. s angl., t. 2. M.: Mir, 1967. 536 s.

10. Skorna G., Ugi I. Isocyanide synthesis with diphosgene // Angewandte Chemie International Edition in English. 1977. N 16. Р. 259–260.

11. Cotarca L., Eckert H. Phosgenations – a handbook. Weinheim: WILEY-VCH Verlag GmbH & Co. KGaA, 2003. 670 р. DOI: 10.1021/op049865d.

12. Golubeva Yu.Yu., Sohadze L.A., Turygin V.V., Derevyagina I.D., Kazakov P.V., Mirzabekova N.S. Poluchenie arildiizocianatov // Himicheskaya promyshlennost’ segodnya. 2019. N 2. S. 22–25.

13. Aresta M., Giannoccaro P., Tommasi I. Carbamoyl complexes as a source of isocyanates or carbamyl chlorides // J. of Organometallic Chemistry. 1994. Vol. 476. P. 13–18.

14. Valli V., Alper H. A simple, convenient, and efficient method for the synthesis of isocyanates from urethanes // J. Organic Chemistry. 1995. Vol. 60. P. 257–258. DOI: 10.1021/jo00106a044.

15. Brase S., Banet K. Organic Azides: Syntheses and applications. John Wiley & Sons, Ltd, Chichester, 2010. 322 p.

16. Skok K.L., Tuinman R.J. New modified liquid pure MDI for CASE applications. URL: https://www.huntsman.com/corporate (data obrashcheniya 01.12.2019).

17. Patent US20080085987A1 C08G18/797. Method of producing a uretonimine-modified isocyanate composition / Th. Savino, S. Bananto, N. Lebedinski; BASF Corp; appl. 2006-10-05; publ. 2008-04-10.

18. Monagle J. Carbodiimides. III. Conversion of isocyanates to var-bodiimides. Catalyst Studies // Journal of Organic Chemistry. 1962. Vol. 27. N 11. P. 3851–3855.

19. Cambell T., Smeltz K. Carbodiimides. IV. High polymers containing the carbodiimide repeat unit // Journal of Organic Chemistry. 1963. Vol. 28. N 8. P. 2069-2075.

20. Polyurethanes. Science, technology, markets, and trends / Mark F. Sonnenschein. John Wiley & Sons International Rights, Inc., 2015. ISBN 978-1-118-73783-5.

__________________________________________________________________

Section III. TEST METHODS FOR SUBSTANCES AND MATERIALS

Pyzhianov I.V., Petrunin V.A., Kondrat′ev V.B.

Reference ion method. III. Quantitative structure – property relationship (qspr) of critical temperature

Federal state unitary enterprise «State scientific-research Institute of organic chemistry and technology» State Scientific Center of Russian Federation,

111024, Moscow, Shosse Entuziastov, 23, e-mail: dir@gosniiokht.ru, tеl.: +7 (495) 673-78-91

Abstract

Global multiple regression model of quantitative structure-property relationship of critical temperature was created by reference ion method. The data with wide chemical diversity were divided into training set of 162 compounds and test set of 29 compounds. Standard deviation of model is 26,8, coefficient of determination – 0,908.

Keywords: quantitative structure-property relationships (QSPR); reference ion method; molecular descriptors; critical temperature; multiple regression; quantum-chemical descriptors.

References

1. Pyzhianov I.V., Petrunin V.A., Kondrat′ev V.B. Quantitative structure property relationship of reduced ion mobility coefficient of organic compounds // Chemistry and Technology of Organic Substances. 2018. N. 1(5). P. 84–101.

2. Pyzhianov I.V., Petrunin V.A., Kondrat′ev V.B. On new approach to study of quantitative structure-property relationships and algorithms for the calculation of molecular descriptors of molecule-ion pair // Chemistry and Technology of Organic Substances. 2018. N. 4 (8). P. 60–75.

3. Pyzhianov I.V., Petrunin V.A., Kondrat′ev V.B. The optimal method for calculation of quantum-chemical molecular descriptors in molecule-ion pairs // Chemistry and Technology of Organic Substances. 2019. N. 2 (10). P. 40-53.

4. Pyzhianov I.V., Petrunin V.A., Kondrat′ev V.B. Reference ion method. I. Quantitative boiling point - structure relationships of organic substances // Chemistry and Technology of Organic Substances. 2019. № 4 (12). С. 33-41.

5. Pyzhianov I.V., Petrunin V.A., Kondrat′ev V.B. Reference ion method. II. Quantitative structure – property relationships of partition octanol - water coefficient // Chemistry and Technology of Organic Substances. 2020. N 1 (13). P. 62–70.

6. Todeschini R., Consonni V. Molecular descriptors for chemoinformatics. 2-nd ed. Weinheim: Wiley-VCH. 2009. Vol. 1. 967 p. DOI: 10.1002/qsar.200330831.

7. Cholakov G., Stateva R., Brauner N., et al. Estimation of Properties of Homologous Series with Targeted Quantitative Structure−Property Relationships // Journal of Chemical & Engineering Data. 2008. Vol. 53. N 11. P. 2510–2520. DOI: 10.1021/je800272x.

8. Bretshnaider S. Svoistva gazov i zhidkostej. M.-L.: Khimia, 1966. 536 s.

9. Rid R., Shervud T. Svoistva gazov i zhidkostei. Izd. 2-е. L.: Khimia, 1971. 704 s.

10. Bouhedjar K., Nacereddine A. K., Ghorab H. et al. QSPR Modeling for critical temperatures of organic compounds using hybrid optimal descriptors: // International Journal of Quantitative Structure-Property Relationships. 2019. Vol. 4. N 4. P. 15–26. DOI: 10.4018/IJQSPR.2019100102.

11. Espinosa G., Yaffe D., Arenas A., et al. A Fuzzy ARTMAP-based quantitative structure−property relationship (QSPR) for predicting physical properties of organic compounds // Ind. Eng. Chem. Res. 2001. Vol. 40. N 12. P. 2757–2766. DOI: 10.1021/ie0008068.

12. Godavarthy S.S., Robinson R.L., Gasem K.A.M. Improved structure–property relationship models for prediction of critical properties // Fluid Phase Equilibria. 2008. Vol. 264. N 1–2. P. 122–136. DOI: 10.1016/j.fluid.2007.11.003.

13. Yaws C.L. Chemical properties handbook: physical, thermodynamic, environmental, transport, safety, and health related properties for organic and inorganic chemicals. New York: McGraw-Hill, 1999. 779 p.

14. Granovsky A.A. Firefly version 8.2. URL: http://classic.chem.msu.su/gran/gamess/pcgamess_home.html (access 14.01.2019).

15. R Core Team. R: A language and environment for statistical computing. R Foundation for Statistical Computing, Vienna, Austria. URL: https://www.R-project.org/ (access 14.01.2019).

16. Golbraikh A., Tropsha A. Beware of q2! // Journal of Molecular Graphics and Modelling. 2002. Vol. 20. N. 4. С. 269–276. DOI: 10.1016/S1093-3263(01)00123-1.

-------------------------------------------------------------------------------------------------

Novikova I.V., Smirnova Zh.V., Novikov R.I., Kurygina L.P.

Determination of β-aminoalcohols in soil by gas chromatography – mass spectrometry

Federal state unitary enterprise «State scientific-research Institute of organic chemistry and technology» State Scientific Center of Russian Federation,

111024, Moscow, Shosse Entuziastov, 23, e-mail: dir@gosniiokht.ru, tеl.: +7 (495) 673-78-91

Abstract

An approach to the codetermination of β-aminoalcohols – precursors and hydrolysis products of toxic nitrogen-containing chemicals in soil by gas chromatography-mass spectrometry was developed. Derivatization conditions of β-aminoalcohols with MTBSTFA were optimized. Sample preparation conditions were determined. It was shown that SPE SCX of the analytes from soil extracts allows the reduction of the matrix effect. The linearity range was 0,5 to 10,0 мкг·мл-1 and the limits of detection for N,N-dialkylaminoethanols – 20–25 ng·ml-1, for N-alkyldiethanolamines – 5–20 ng·ml-1 and for 3-quinuclidinol – 50 ng·ml-1.

Keywords: β-aminoalcohols; derivatization; gas chromatography; mass spectrometry; soil samples.

References

1. Recommended operating procedures for analysis in the verification of chemical disarmament / Editor: P.Vanninen. The Ministry for foreign affairs of Finland, University of Helsinki, 2017. 809 p. ISBN 978-951-51-3917-7.

2. Munro N.B., Talmage S.S., Griffin G.D. et al. The sources, fate, and toxicity of Chemical Warfare Agent degradation products // Environmental Health Perspectives. 1999. Vol. 107. N 12. P. 933–974. DOI:10.1289/ehp.99107933.

3. Konvencija o zapreshhenii razrabotki, proizvodstva, nakoplenija i primenenija himicheskogo oruzhija i o ego unichtozhenii. Mezhdunarodnaya konferencija po podpisaniyu Konvencii. GE. 92–61926, Parizh, 1993. Byulletenʼ mezhdunarodnyh dogovorov. 1998. N 4. S. 3–116.

4. Dubey D.K., Pardasani D., Palit M. et al. On-matrix derivatisation – extraction of precursors of nitrogen- and sulfur-mustards for veriﬁcation of chemical weapons convention // Journal of Chromatography A. 2005. Vol. 1076. P. 27–33.

DOI: 10.1016/j.chroma.2005.04.066.

5. Chinthakindi S., Purohit A., Singh V. et al. On-matrix derivatization extraction of chemical weapons convention relevant alcohols from soil // Journal of Chromatography A. 2013. Vol. 1311. P. 170–175. DOI: 10.1016/j.chroma.2013.08.079.

6. Zaikin V.G., Mikaja А.I. Himicheskie metody v mass-spectrometrii organicheskih soedinenij. М.: Nauka, 1987. 200 s.

7. Blau K., Halket J. Handbook of derivatives for chromatography. John Wiley & Sons Ltd, 1993. 369 p. ISBN 0-471-92699-X.

8. Kashutina M.V., Ioffe S.L., Tartakovskij V.А. Sililirovanie organicheskih soedinenij // Russian Chem. Reviews. 1975. Vol. 44. N 9.P. 733–747. DOI: 10.1070/RC1975v044n09ABEH002373.

9. Valdez C.A., Leif R.N., Hart B.R. Rapid and mild silylation of β-amino alcohols at room temperature mediated by N-methylimidazole for enhanced detectability by gas chromatography/electron ionization mass spectrometry // Rapid communications in mass spectrometry. 2014. Vol. 28. P. 2217–2221.

10. Bajgilʼdiev Т.М., Vokuev М.F., Oreshkin D.V. i dr. n-Metoksifenacilbromid – universalʼnyj reagent dlya opredeleniya alkilfosfonovyh i alkilmetilfosfonovyh kislot metodami vysokoeffektivnoj zhidkostnoj i gazovoj hromatografii s massspektrometricheskim detektirovaniem // Mass-spectrometriya. 2019. Т. 16. N 3, S. 180-190.

11. Ohsawa I., Seto Y. Determination of nitrogen mustard hydrolysis products, ethanolamines by gas chromatography–mass spectrometry after tert-butyldimethylsilyl derivatization // Journal of Chromatography A. 2006. Vol. 1122. P. 242–248. DOI: 10.1016/j.chroma.2006.04.076.

12. Kanaujia P. K., Tak V., Pardasani D. et al. Application of cation-exchange solid-phase extraction for the analysis of amino alcohols from water and human plasma for verification of Chemical Weapons Convention // Journal of Chromatography A. 2008. Vol. 1185. P. 167–177. DOI: 10.1016/j.chroma.2008.01.080.

13. NIST/EPA/NIH. NIST Mass Spectral Library. National Institute of Standards and Technology, US Secretary of Commerce: USA, 2017.

14. OPCW Central Analytical Database, OCAD v. 22, Technical Secretariat of the Organization for the Prohibition of Chemical Weapons, 2020.

15. OPCW Validation Group Working Database, VGWD-2020, Technical Secretariat of Organization for the Prohibition of Chemical Weapons, 2020.

-----------------------------------------------------------------------------------------------

Klimov D.I., Kostikova N.A., Kaabak L.V., Shibkov O.O., Cherenkov M.A., Pyzh’yanov I.V.

Research of acid catalysis mechanism of the reaction of obtaining N-phenyl-2-naphthylamine from 2-naphthol and aniline

Federal state unitary enterprise «State scientific-research Institute of organic chemistry and technology» State Scientific Center of Russian Federation,

111024, Moscow, Shosse Entuziastov, 23, e-mail: dir@gosniiokht.ru, tеl.: +7 (495) 673-78-91

Abstract

Analysis of existing hypotheses of acid catalysis of the synthesis of N-phenyl-2-naphthylamine from 2-naphthol and aniline was carried out. Quantum chemical studies were performed to calculate the thermodynamic and electronic components of models of probable intermediate particles formed during the reaction under the catalytic action of mineral acids. The results obtained in the course of experimental and theoretical studies allowed us to put forward a hypothesis about the mechanism of acid catalysis of the reaction between 2-naphthol and aniline in the presence of phosphoric acid.

Keywords: N-phenyl-2-naphthylamine; 2-naphthol; aniline; reaction mechanism; acid catalysis, quantum chemical calculation.

References

1. Gorbunov B.N., Gurevich Ya.A., Maslova I.P. Khimiya i tekhnologiya stabilizatorov polimernykh materialov. M .: Khimiya, 1981.

2. Yang J.C., Niu D., Karsten B.P. et al. Use of a “catalytic” cosolvent, N,N-dimethyl octanamide, allows the flow synthesis of imatinib with no solvent switch // Angewandte Chemie (International ed. in English). 2016. Vol. 55 (7). P. 2531–2535. DOI: 10.1002/anie.201509922.

3. Mishra A.K., Biswas S. Brønsted acid catalyzed functionalization of aromatic alcohols through nucleophilic substitution of hydroxyl group // Journal of Organic Chemistry. 2016. Vol. 81. P. 2355–2363. DOI: 10.1021/acs.joc.5b02849.

4. Iglesias M.J., Blandez J.F., Fructos M.R. et al. Synthesis, structural characterization and catalytic activity of IPrNi(styrene)2 in the amination of aryl tosylates // Organometallics. 2012. Vol. 31. N 17. P. 6312–6316. DOI: 10.1021/om300566m.

5. Gao C.-Y.,Yang L.-M. Nickel-catalyzed amination of aryl tosylates // Journal of Organic Chemistry. 2008. Vol. 73. N 4. P. 1624–1627. DOI: 1021/jo7022558.

6. Tundel R. E., Anderson K. W., Buchwald S.L. Expedited palladium-сatalyzed amination of aryl nonaflates through the rse of microwave-irradiation and soluble organic amine bases // Journal of Organic Chemistry. 2006. Vol. 71. N 1. P. 430–433. DOI: 10.1021/jo052131u.

7. Keesara S. N-(Pyridin-2-yl)benzamide: efficient ligand for the nickel catalyzed Chan–Lam cross-coupling reaction // Tetrahedron Letters. 2015. Vol. 56. N 48. P. 6685–6688. DOI: 10.1016/j.tetlet.2015.10.047.

8. Roy S., Sarma M., Kashyap B., Phukan P. A quick Chan–Lam C–N and C–S cross coupling at room temperature in the presence of square pyramidal [Cu(DMAP)4I]I as a catalyst // Chemical Communications. 2016. Vol. 52. N 6. P. 1170–1173. DOI: 10.1039/C5CC04619J.

9. Reddy S.B.V., Reddy N.S., Reddy Y.J., Reddy Y.V. Indium/Cu(II)-mediated one-pot synthesis of unsymmetrical diaryl amines from aryl boronic acids and azides // Tetrahedron Letters. 2011. Vol. 52. N 20. P. 2547–2549. DOI: 10.1016/j.tetlet.2011.03.022.

10. Vantourout J.C., Law R.P., Isidro-Llobet A., Atkinson S., Watson A.J. B. Chan–Evans–Lam amination of boronic acid pinacol (BPin) esters: Overcoming the aryl amine problem // Journal of Organic Chemistry. 2016. Vol. 81. N 1. P. 3942–3950. DOI: 10.1021/acs.joc.6b00466.

11. Musolino B.J., Kabalka G.W. Copper mediated formation of carbon-heteroatom bonds using organoboron reagents and ultrasound // Heterocycles. 2015. Vol. 90. P. 271–297. DOI: 10.3987/COM-14-S(K)18.

12. Yang J., Li P., Zhang Y., Wang L. A new library of arsine, stibine-stabilized 
N-heterocyclic carbene palladium complexes: synthesis, structures and activities in C–C and C–N coupling reactions // Dalton Transaction. 2014. Vol. 43. N 37. P. 14114–14122. DOI: 10.1039/C4DT01773K.

13. Patent 2013069049 US, C07D495/04. Compound comprising a five-membered hetero ring, an organic electrical element using the same and a terminal thereof; Duksan High Metal Co., Ltd.; appl. 2010-05-26; publ. 2015-04-14.

14. Kurandina D.V., Eliseenkov E.V., Petrov A.A., Boyarskiy V.P. N(2)-Monosubstituted bishydrazides of oxalic acid as new efficient components of the system for the copper-catalyzed C-N cross-coupling in water // Russian Chemical Bulletin. 2012. Vol. 61. N 5. P. 1009–1012. DOI: 10.1007/s11172-012-0130-6.

15. Kurandina D.V., Eliseenkov E.V., Petrov A.A., Boyarskiy V.P. Effect of the structural factors on reactivity of aryl halides in the copper-catalyzed arylation of aniline in aqueous medium // Russian Journal of General Chemistry. 2015. Vol. 85. N 10. P. 2277–2281. DOI: 10.1134/S1070363215100096.

16. Udyma P.G. Bor’ba s korroziyey oborudovaniya v proizvodstve poluproduktov i krasiteley. M .: Goskhimizdat, 1957. 159 s.

17. Pakhomov V. S. Korroziya metallov i splavov: cpravochnik: v 2 kn. M.: Nauka i tekhnologiya, 2013. Kn. 2. 544 c.

18. Efros L.S., Kvitko I.Y. Khimiya i tekhnologiya aromaticheskih soedinenii v zadachah i upragneniyah. Uchebnoe posobie dlya vuzov. 2-e izd. pererab. L.: Khimiya, 1980. 416 s.

19. Serrej A. Spravochnik po organicheskim reakciyam: Imennye reakcii v organicheskoj himii. M.: Goshimizdat, 1962. 300 s.

20. Smith M., March М. March’s advanced organic chemistry: reactions, mechanisms and structure. John Wiley & Sons, 2007. P. 882–883. ISBN 9780471720911.

21. Jensen F. Introduction to computational chemistry. 2nd ed. Chichester, England; Hoboken, NJ: John Wiley & Sons, 2007. 599 p. ISBN-13: 978-0-470-01186-7.

22. Young D.C. Computational chemistry: a practical guide for applying techniques to real world problems. New-York: Wiley, 2001. 434 p. ISBN: 0-471-33368-9.

23. Pyzhianov I.V., Petrunin V.A., Kondratiev V.B. The optimal method for calculation of quantum chemical molecular descriptors in molecule – ion pairs // Chemistry and Technology of Organic Substances. 2019. N 2 (10) P. 40 – 53 (in Rus.).

24. NIST Chemistry WebBook. URL: https://webbook.nist.gov/chemistry/ (data obrashcheniya: 12.04.2019).

25. Antonova M.M., Kostikova N.A., Golikov A.G., Klimov D.I. Highly efficient method of producing neozone d // Chemistry and Technology of Organic Substances. 2018. N 1 (5). S. 9-18.

26. Patent 2676692 RF, S07S211 / 60, S07S209 / 18. Sposob polucheniya N-fenil-2-naftilamina; Kondrat’yev V.B., Golikov A.G., Kazakov P.V., Kostikova N.A., Klimov D.I., Antonova M.M .; zayavl. 01.08.2018, opubl. 10.01.2019.

27. Chchibabin A.E. Osnovnye nachala organicheskoj Khimii. Tom 2. M.: Goshimizdat, 1957. 676 s.

28. MI «Metodika (metod) izmereniy obshchikh doley letuchikh veshchestv v 
N-fenil-2-naftilamine gravimetricheskim metodom» (svidetel’stvo o poverke ot 14 aprelya 2017 g. № 310003.03 / 37-2017).